## Slide 1: Switching Techniques

## Slide 2: Switching Terms
Switching Nodes:
  Intermediate switching device that moves data
  Not concerned with content of data
Stations:
  End devices that wish to communicate
  Each station is connected to a switching node
Communications Network:
  A collection of switching nodes

## Slide 3: Switched Network

## Slide 4: Observations of Figure 3.3
Some nodes connect only to other nodes (e.g., 5 and 7)
Some nodes connect to one or more stations
Node-station links usually dedicated point-to-point links
Node-node links usually multiplexed links
  Frequency-division multiplexing (FDM)
  Time-division multiplexing (TDM)
Not a direct link between every node pair

## Slide 5: Techniques Used in Switched Networks
Circuit switching
  Dedicated communications path between two stations
  E.g., public telephone network
Packet switching
  Message is broken into a series of packets
  Each node determines next leg of transmission for each packet

## Slide 6: Phases of Circuit Switching
Circuit establishment
  An end to end circuit is established through switching nodes
Information Transfer
  Information transmitted through the network
  Data may be analog voice, digitized voice, or binary data
Circuit disconnect
  Circuit is terminated
  Each node deallocates dedicated resources

## Slide 7: Components of Public Telecommunications Network
Subscribers - devices that attach to the network; mostly telephones
Subscriber line - link between subscriber and network
  Also called subscriber loop or local loop
Exchanges - switching centers in the network
  A switching centers that support subscribers is an end office
Trunks - branches between exchanges

## Slide 8: Characteristics of Circuit Switching
Can be inefficient
  Channel capacity dedicated for duration of connection
  Utilization not 100%
  Delay prior to signal transfer for establishment
Once established, network is transparent to users
Information transmitted at fixed data rate with only propagation delay

## Slide 9: How Packet Switching Works
Data is transmitted in blocks, called packets
Before sending, the message is broken into a series of packets
  Typical packet length is 1000 octets (bytes)
  Packets consists of a portion of data plus a packet header that includes control information
At each node en route, packet is received, stored briefly and passed to the next node

## Slide 10: Packet Switching

## Slide 11: Packet Switching

## Slide 12: Packet Switching Advantages
Line efficiency is greater
  Many packets over time can dynamically share the same node to node link
Packet-switching networks can carry out data-rate conversion
  Two stations with different data rates can exchange information
Unlike circuit-switching networks that block calls when traffic is heavy, packet-switching still accepts packets, but with increased delivery delay
Priorities can be used

## Slide 13: Disadvantages of Packet Switching
Each packet switching node introduces a delay
Overall packet delay can vary substantially
  This is referred to as jitter
  Caused by differing packet sizes, routes taken and varying delay in the switches
Each packet requires overhead information
  Includes destination and sequencing information
  Reduces communication capacity
More processing required at each node

## Slide 14: Packet Switching Networks - Datagram
Each packet treated independently, without reference to previous packets
Each node chooses next node on packet’s path
Packets don’t necessarily follow same route and may arrive out of sequence
Exit node restores packets to original order
Responsibility of exit node or destination to detect loss of packet and how to recover

## Slide 15: Packet Switching Networks – Datagram
Advantages:
  Call setup phase is avoided
  Because it’s more primitive, it’s more flexible
  Datagram delivery is more reliable

## Slide 16: Packet Switching Networks – Virtual Circuit
Preplanned route established before packets sent
All packets between source and destination follow this route
Routing decision not required by nodes for each packet
Emulates a circuit in a circuit switching network but is not a dedicated path
  Packets still buffered at each node and queued for output over a line

## Slide 17: Packet Switching Networks – Virtual Circuit
Advantages:
  Packets arrive in original order
  Packets arrive correctly
  Packets transmitted more rapidly without routing decisions made at each node

## Slide 18: Effect of Packet Size on Transmission

## Slide 19: Effect of Packet Size on Transmission
Breaking up packets decreases transmission time because transmission is allowed to overlap
Figure 3.9a
  Entire message (40 octets) + header information (3 octets) sent at once
  Transmission time: 129 octet-times
Figure 3.9b
  Message broken into 2 packets (20 octets) + header (3 octets)
  Transmission time: 92 octet-times

## Slide 20: Effect of Packet Size on Transmission
Figure 3.9c
  Message broken into 5 packets (8 octets) + header (3 octets)
  Transmission time: 77 octet-times
Figure 3.9d
  Making the packets too small, transmission time starts increases
  Each packet requires a fixed header; the more packets, the more headers

## Slide 21: Asynchronous Transfer Mode (ATM)
Also known as cell relay
Operates at high data rates
Resembles packet switching
  Involves transfer of data in discrete chunks, like packet switching
  Allows multiple logical connections to be multiplexed over a single physical interface
Minimal error and flow control capabilities reduces overhead processing and size
Fixed-size cells simplify processing at ATM nodes

## Slide 22: ATM Terminology
Virtual channel connection (VCC)
  Logical connection in ATM
  Basic unit of switching in ATM network
  Analogous to a virtual circuit in packet switching networks
  Exchanges variable-rate, full-duplex flow of fixed-size cells
Virtual path connection (VPC)
  Bundle of VCCs that have the same end points

## Slide 23: Advantages of Virtual Paths
Simplified network architecture
Increased network performance and reliability
Reduced processing and short connection setup time
Enhanced network services

## Slide 24: Call Establishment

## Slide 25: Virtual Channel Connection Uses
Between end users
  Can carry end-to-end user data or control signaling between two users
Between an end user and a network entity
  Used for user-to-network control signaling
Between two network entities
  Used for network traffic management and routing functions

## Slide 26: Virtual Path/Virtual Channel Characteristics
Quality of service
  Specified by parameters such as cell loss ratio and cell delay variation
Switched and semipermanent virtual channel connections
Cell sequence integrity
Traffic parameter negotiation and usage monitoring
Virtual channel identifier restriction within a VPC

## Slide 27: ATM Cell Header Format
Generic flow control (GFC) – 4 bits, used only in user-network interface
  Used to alleviate short-term overload conditions in network
Virtual path identifier (VPI) – 8 bits at the user-network interface, 12 bits at network-network interface
  Routing field
Virtual channel identifier (VCI) – 8 bits
  Used for routing to and from end user

## Slide 28: ATM Cell Header Format
Payload type (PT) – 3 bits
  Indicates type of information in information field
Cell loss priority (CLP) – 1 bit
  Provides guidance to network in the event of congestion
Header error control (HEC) – 8 bit
  Error code

## Slide 29: ATM Service Categories
Real-time service
  Constant bit rate (CBR)
  Real-time variable bit rate (rt-VBR)
Non-real-time service
  Non-real-time variable bit rate (nrt-VBR)
  Available bit rate (ABR)
  Unspecified bit rate (UBR)

## Slide 30: Examples of CBR Applications
Videoconferencing
Interactive audio (e.g., telephony)
Audio/video distribution (e.g., television, distance learning, pay-per-view)
Audio/video retrieval (e.g., video-on-demand, audio library)

## Slide 31: Examples of UBR applications
Text/data/image transfer, messaging, distribution, retrieval
Remote terminal (e.g., telecommuting)