## Slide 1: TRANSMISSION LOSS

## Slide 2: SIGNAL LOSS
Signal emitted from the source is never received as it is at the destination due to various reasons, called signal or information loss

## Slide 3: TRANSMISSION IMPAIRMENTS ONTOLOGY
ATTENUATION
FREE SPACE LOSS
NOISE
ATMOSPHERIC ABSORPTION
MULTIPATH
REFRACTION

## Slide 4: ATTENUATION
Loss of signal strength
For guided media it is logarithmic function of distance
For Unguided media it is combination of distance and medium’s functions
Targets
    Signal must maintain enough strength to be interpreted properly by receiver's Circuitry
    Signal level must be higher than noise to be received error free
    Higher Frequencies, more attenuation, distortion

## Slide 5: FREE SPACE LOSS
Signal loss even in the absence of attenuation
More significant in case of Satellite Comm.
Generalized Expression

## Slide 6: NOISE
Additional unwanted signal
Classes
    Thermal Noise
    Intermodulation Noise
    Cross Talk
    Impulse Noise

## Slide 7: ATMOSPHERIC ABSORPTION
Water vapors
Oxygen
Peak at 22GH extreme at 60
Lowers at 15 GH
Rain, Fog etc

## Slide 8: Multipath
Due to reflection or so signal follows more than one path
Receiver gets multiple copies

## Slide 9: Refraction
Passing through the second medium
Path change